## Slide 1: IFC4 Reference View Geometry
Comparison of approaches
Tim Chipman
buildingSmart Model Support Group

## Slide 2: Reference View Geometry
Since geometry does not need to be edited, it should be represented in the most simple form possible, so long as that doesn’t negatively impact other considerations such as file size or resulting RAM size
Tessellation (triangles + vertices) proposed for re-usable shapes
Mapped geometry (positioning + scaling) proposed for repetition
All other geometry (CSG, NURBS, Extrusions, Primitives, BREP) out of scope unless other considerations proven to be negatively impacted

## Slide 3: Implementation Overhead
Requires more processing time, slower rendering
Increases software development time/cost
IfcFacetedBrep: requires tessellation of faces
IfcSweptSolid/IfcCsgSolid: requires converting to IfcFacetedBrep
IfcArbitraryClosedProfileDef: requires converting to IfcPolyline – IfcTrimmedCurve, IfcBSplineCurve, IfcCompositeCurve, …
IfcParameterizedProfileDef: requires converting to IfcArbitraryClosedProfileDef

## Slide 4: Scenarios
Equipment – fixed geometry defined on type
  Type: IfcTriangulatedFaceSet
  Occurrence: IfcMappedItem – single item
Walls – rectangular geometry with openings for doors, windows
  Type: may or may not use shared type for tessellation
  Occurrence: IfcTriangulatedFaceSet – no normal vectors
Piping – circular
  Type: IfcTriangulatedFaceSet – cylinder for segments, torus arc for bends
  Occurrence: IfcMappedItem – multiple items

## Slide 5: Geometry object referencing
Object references can be arbitrarily interned in files and in memory
IfcElement
IfcShapeRepresentation
IfcElement
IfcElement
IfcMappedItem
IfcShapeRepresentation
IfcElement
IfcShapeRepresentation
IfcMappedItem
IfcRepresentationMap
IfcShapeRepresentation
Same shape, different position or size
Same position & size, different combinations
Same geometry,
different object placement

## Slide 6: Tessellated Geometry: Curved Surfaces
Normal vectors defined to interpolate lighting
Provides the illusion of rounded surfaces without increasing points
Increasing the number of segments in a circle increases realism, but requires more CPU and GPU resources
If ends aren’t visible (e.g. pipes), 8 segments generally sufficient
If ends are visible, 16 is better

## Slide 7: Tessellated Geometry: Resource Usage
Flat geometry (no normal vectors) #10000=IfcTriangulatedFaceSet(#10001,$,.TRUE.,((11,22,33),),$); #10001=IfcCartesianPointList3D((1.1111,2.2222,3.3333),);
File Size: 89+23*VertexCount+11*FaceCount RAM Size: 8*(15+3*VertexCount+3*FaceCount)
Curved geometry (normal vectors specified) #10000=IfcTriangulatedFaceSet(#10001,((0.3333.,0.6666,0.),),.TRUE.,((11,22,33),),((11,22,33),); #10001=IfcCartesianPointList3D((1.1111,2.2222,3.3333),);
File Size: 89+23*VertexCount+22*FaceCount+20*Normals RAM Size: 8*(15+3*VertexCount+6*FaceCount+3*Normals)

## Slide 8: Example comparison for piping network
Minimal tessellated shapes:
  Cylinder – for pipe segments
  Torus Arc – for pipe fittings
Occurrences uses multiple mapped items

## Slide 9: Comparison of Swept Disk Solid vs. Mapped
#10000=IfcShapeRepresentation(#1,’Body’,’AdvancedSweptSolid’,(#10001)); #10001=IfcSweptDiskSolid(#10002,0.125,0.120,$,$); #10002=IfcCompositeCurve((#10003,#10004,),.FALSE.); #10003=IfcPolyLine(($10004,#10005)); #10004=IfcCartesianPoint((1.1111,2.2222,3.3333)); #10005=IfcCartesianPoint((1.1111,2.2222,4.4444)); #10006=IfcTrimmedCurve(#10007,IfcParameterValue(0.0),IfcParameterValue(0.25),.TRUE.,.PARAMETER.); #10007=IfcCircle(#10008,0.5); #10008=IfcAxis2Placement3D(#10009,#10010,#10011); #10009=IfcCartesianPoint((1.1111,2.2222,3.3333); #10010=IfcDirection(1.0,0.0,0.0); #10011=IfcDirection(0.0,1.0,0.0); File Size: 1488 characters = 153 + 144 * SegmentCount + 301 * FittingCount [use 3 segments, 3 fittings] RAM Size: 1784 bytes = 8*(24 + 27 * SegmentCount + 39 * FittingCount) [16 bytes per instance, 8 per field, 16 per array, strings interned]
#10000=IfcShapeRepresentation(#1,’Body’,’MappedRepresentation’,(#10001,#10004,)); #10001=IfcMappedItem(#20000); #10002=IfcCartesianTransformationOperator3DnonUniform($,$,#10003,$,$,$,4.0); #10003=IfcCartesianPoint((1.1111,2.2222,3.3333)); #10004=IfcMappedItem(#10005); #10005=IfcCartesianTransformationOperator3D($,$,#10006,1.0,$); #10006=IfcCartesianPoint((1.1111,2.2222,3.3333));
File Size: 984 characters = 69 + 165 * SegmentCount + 141 * FittingCount RAM Size: 1056 bytes = 8*(9 + 22 * SegmentCount + 19 * FittingCount)

## Slide 10: Comparison of Swept Disk Solid vs. Mapped
Geometry | File Size (bytes) | Memory Size (bytes)
IfcSweptDiskSolid | 1488 | 1784
IfcMappedItem | 984 | 1056
Mapped tessellation is more efficient
34% smaller IFC file sizes
41% smaller memory usage
However, if ‘Axis’ curve is already defined, then IfcSweptDiskSolid has no additional file size -- should ‘Axis’ be defined in Reference View?
Memory is allocated for tessellated geometry in all cases

## Slide 11: Comparison of Extruded Solid vs. Mapped
#10000=IfcShapeRepresentation(#1,’Body’,’SweptSolid’,(#10001)); #10001=IfcExtrudedAreaSolid(#10005,#10002,#10004,4.0); #10002=IfcAxis2Placement3D(#10003,$,$); #10003=IfcCartesianPoint(0.,0.,0.); #10004=IfcDirection(0.,0.,1.0); #10005=IfcArbitraryClosedProfileDef(.AREA.,$,#10006); #10006=IfcPolyline((#10007,#10008,#10009,#10010,#10011)); #10007=IfcCartesianPoint((0.,0.)); #10008=IfcCartesianPoint((8.,0.)); #10008=IfcCartesianPoint((8.,4.)); #10010=IfcCartesianPoint((0.,4.));
#10000=IfcShapeRepresentation(#1,’Body’,’SweptSolid’,(#10001)); #10001=IfcExtrudedAreaSolid(#10005,#10002,#10004,4.0); #10002=IfcAxis2Placement3D(#10003,$,$); #10003=IfcCartesianPoint(0.,0.,0.); #10004=IfcDirection(0.,0.,1.0); #10005=IfcRectangleProfileDef(.AREA.,$,8.,4.);
#10000=IfcShapeRepresentation(#1,’Body’,’MappedRepresentation’,(#10001)); #10001=IfcMappedItem(#20000); #10002=IfcCartesianTransformationOperator3DnonUniform($,$,#10003,$,8.0,$,4.0); #10003=IfcCartesianPoint((1.1111,2.2222,3.3333));
Extruded Arbitrary Profile
File Size: 479, RAM Size: 504
Extruded Rectangle Profile
File Size: 274, RAM Size: 296
Mapped (Tessellation or other):
File Size: 233, RAM Size: 224

## Slide 12: Comparison of Extruded Solid vs. Mapped
IfcMappedItem is most efficient (mapped tessellation or other)
IfcTriangulatedFaceSet at every occurrence is more efficient than extruded arbitrary profile, a bit less efficient than extruded rectangle
If wall has openings, then extruded geometry wouldn’t work, so would have to use tessellation to avoid Boolean operations
Geometry | File Size (bytes) | Memory size (bytes)
IfcExtrudedAreaSolid+IfcArbitraryClosedProfileDef | 479 | 504
IfcExtrudedAreaSolid+IfcRectangleProfileDef | 274 | 296
IfcMappedItem | 233 | 224
IfcTriangulatedFaceSet (8 points, 6 faces) re-used | 345 | 456